## Slide 1: Line Sensor (Feedback For Autonomous Operation)
Chassis
Motor
Motor IC
RPI
ADC IC
Line sensor
Line sensor detects if there is a line on the floor
Consists of 2 elements
  Line sensor
  ADC which stands for Analog-to-digital converter ( 8channels)
Raspberry pi will talk to the ADC chip with SPI bus
  SPI stands for Serial Peripheral Bus.
  High speed serial bus
Motor

## Slide 2: Feedback Control, Autonomous mode
Keyboard inputs
PWM signal using GPIO pins
Directional and Speed Control
Sensor inputs
PWM signal using GPIO pins
Directional and Speed Control
Feedback Control
Read voltage of 8 sensors
Make a decision on where the line is relative to the 8 sensors
Generate Error signals: how much is the offset from center or going straight. Left and Right wheels have separate error signals
Use the error signals to decide how to drive the 2 PWM GPIO pins
USER CONTROL
AUTONOMOUS

## Slide 3: How Does The LineSensor Work
If there is reflection from the floor, then the light sensitive transistor will turn on the voltage will be low
If there is no reflection, ie a black surface where the light is absorbed, then the light sensitive transistor is off and voltage is high
Purpose of ADC
  Measure the voltage
  convert to 10 bits number
Python driver
  Read the 10 bit number
  Decide if a line is present by comparing it to a threshold voltage
ADC

## Slide 4: Line Sensor Top View
Infra-Red transmit LED
Light Sensitive transistor
Header pins for voltage sense
3.3V power and ground

## Slide 5: Wiring Line Sensors
3.3V
3.3V
GND
GPIO11 (SPI0_SCLK)
GPIO09 (SPI0_MISO)
GPIO10 (SPI0_MOSI)
GND
GPIO8 (SPI0_CS0)
Analog-to-digital Converter
Line
RPI GPIO Pin Connections
10 wires Ribbon cable

## Slide 6
asdfsf
Line sensors nearer to the caster wheels
VCC
GND
Front row

## Slide 7: Steering Control
Steering is achieved by having a differential speed between the left wheels and right wheels
DiffSPD = abs(LeftWheelSpeed – RightWheelSpeed)
Left Turn
Left Drift
Forward
Reverse
Right Turn
Right Drift

## Slide 8: Error Signal Generations
7
6
5
4
3
2
1
0
Line
7
6
5
4
3
2
1
0
Line
7
6
5
4
3
2
1
0
Line
Steer Straight, no error
No differential speed
7
6
5
4
3
2
1
0
Line
Error, steer left
RightError = LINE_DETECT[2] + (LINE_DETECT[1] * 4.) = 0
LeftError = LINE_DETECT[5] + (LINE_DETECT[6] * 4.) = 1
Error, steer left
RightError = LINE_DETECT[2] + (LINE_DETECT[1] * 4.) = 0
LeftError = LINE_DETECT[5] + (LINE_DETECT[6] * 4.) =4
Error, steer right
RightError = LINE_DETECT[2] + (LINE_DETECT[1] * 4.) = 1
LeftError = LINE_DETECT[5] + (LINE_DETECT[6] * 4.) =0
7
6
5
4
3
2
1
0
Line
Error, steer right
RightError = LINE_DETECT[2] + (LINE_DETECT[1] * 4.) = 4
LeftError = LINE_DETECT[5] + (LINE_DETECT[6] * 4.) =0

## Slide 9: Using Error Signal For Steering Control
0
1
2
3
4
5
6
7
Line
0
1
2
3
4
5
6
7
Line
0
1
2
3
4
5
6
7
Line
0
1
2
3
4
5
6
7
Line
Steer Straight, no error
No differential speed
Error, steer left
PIN_SPD = AvgVar + (DiffSPD/2) # left
PIN_SPD2 = AvgVar - (DiffSPD/2) #right
Error, steer left
RightError = LINE_DETECT[2] + (LINE_DETECT[1] * 4.) = 0
LeftError = LINE_DETECT[5] + (LINE_DETECT[6] * 4.) = 1
right = RightError
left = LeftError
# amplify error, assuming left > 0
DiffSPD = Kp * left
PIN_SPD = AvgVar + (DiffSPD/2) # left
PIN_SPD2 = AvgVar - (DiffSPD/2) #right
AvgVar is the average speed
pi.set_PWM_dutycycle(PIN_1, PIN_SPD) pi.set_PWM_dutycycle(PIN_3, PIN_SPD2)